# GUIDELINES FOR Sidra Analysis Draft v 1.0

## Purpose

Transport Canberra and City Services (TCCS) is currently reviewing the Guidelines for SIDRA Analysis to assist the traffic and transport practitioners for intersection modelling.

## Background

For SIDRA modelling purpose, TCCS has adopted the Roads and Maritime Services (RMS) NSW Traffic Modelling Guidelines (version 1.0, 2013) as its primary technical reference, unless and otherwise specified explicitly in this note. It is advised that practitioners refer to Chapter 14 in this document and Appendix E on gap acceptance parameters.

If a SIDRA parameter is not mentioned within the guideline then the default value should be used. If practitioners wish to adopt alternative settings and/or parameters, their use should be noted and justified in the accompanying traffic study report.

## Traffic Counts

The time when the traffic counts were taken (i.e. 15-18 November 2016) and any assumptions regarding turning proportions should be noted. For modelling existing conditions, if the traffic counts are greater than one year old, then the traffic growth needs to be established using the approaches outlined in section 4.6. If data on growth is limited, then a growth rate is to be determined from historical traffic counts where possible otherwise a base growth rate of 2% per annum can be used.

## Traffic Signals

### For existing sites:

It should be noted that the default signals parameters in the SIDRA can significantly vary from existing signals operation parameters. Therefore to achieve the accuracy of models, the practitioner should obtain signals operation information from the Roads ACT and modify the input parameters accordingly.

On request, Roads ACT provides ‘SCATS Summaries’ tech notes which outlines the existing signals controller settings such as cycle length, phase timings, minimum green, inter-green, pedestrian crossing times, and coordination details (see Appendix A).

For complex intersections such as median approaches (e.g. Northbourne Avenue/Bunda Street/Rudd Street), staggered intersections, closely spaced intersections (e.g. Newcastle Street between Monaro Highway ramps and Gladstone Street), the practitioners/modellers are suggested to discuss and confirm with Roads ACT on the scope of network and methodology before undertaking modelling.

### For new or proposed upgraded sites:

- Consult Roads ACT to confirm signals controller information such as cycle time, phasing and sequence, minimum green, inter green (yellow/red), and pedestrian clearance times (walk + clearance).

By default, it is suggested to consider 8 sec minimum green, 4 sec and 5 sec yellow for 60 km/h and 80 km/h road speed limit respectively.

- The intersection performance should be assessed against to the future design years (2021 and 2031) and must satisfy the following performance criteria:

| SIDRA output parameter | New Signals |
| --- | --- |
| Degree of Saturation | ≤ 0.9 |
| Level of Service (LOS) – Delay RTA NSW method | “E” or better |

### Models reporting requirements

- Electronic SIDRA Intersection Project (.SIP) files for base case and all scenario models.

- For easy comparison, tables and/or figures should be provided showing base and option model inputs/outputs details such as (see Appendix C):

  - Intersection geometry

  - Input volumes summary

  - Movement  summary

  - Lane summary

  - Phasing summary

- Traffic data and signals controller info (SCATS summaries) used for modelling

- Design drawings/plans for proposed intersection treatments showing the geometry layouts

### Key checks

To assess the validity and robustness of models, Roads ACT undertakes technical reviews on the submitted models. Appendix D outlines the key aspects considered during the review. It is suggested that the practitioners use this checklist to:

- Verify base models, prior to start developing option/test models

- Verify models, prior to the TIA submission.

## Appendix A – SCATS Summary example

Set 199 – Eastern Valley Way/Cameron Avenue/Aikman Drive, Belconnen

Site details

- Single Diamond Operation (SDO) on Eastern Valley Way, and Split Approach (SA) on Aikman Drive and Cameron Avenue.

- Phase sequence: A-D-E-F at all times.

Right turn operation

- Right turns on Eastern Valley way are fully controlled (i.e. no filters).

Phase time and cycle length details

- Maximum cycle time is 110 sec

- Average phase time (sec) and cycle length (sec) details on 20-22 October 2015:

| Peak | Time Period | Avg CL | A | D | E | F/ F1* |
| --- | --- | --- | --- | --- | --- | --- |
| AM | 0800-0900 | 100 | 39 | 17 | 29 | 15 |
| Business | 1400-1500 | 85 | 33 | 20 | 18 | 14 |
| PM | 1700-1800 | 110 | 34 | 33 | 21 | 22 |
| Minimum Green time (sec) | 8 | 8 | 8 | 8 |
| Yellow Time (sec) | 4 | 4 | 4 | 4 |
| Red Time (sec) | 2 | 3 | 3 | 2 |
| Intergreen time (Yellow + Red) | 6 | 7 | 7 | 6 |

- *Right turns from north ran only 12 times (out of 36 cycles) in AM peak, 17 times (out of 42 cycles) in business peak, and 15 times (out of 33 cycles) in PM peak. This means, F1 phase ran a considerable number of times in peak periods.

Linking

- None

SIDRA coordination

- Eastern Valley Way south  and Aikman Drive is ‘favourable’ in all peak periods.

- All other approaches are ‘not favourable’ in any period.

## Pedestrian timings

| Ped walk | Vehicle phase(s) | Walk+ clearance time (in sec) |
| --- | --- | --- |
| P1 | A, F1 | 20 |
| P2 | A, F2 | 22 |
| P3 | D | 14 |
| P4 | D, E | 20 |
| P5 | E | 14 |
| P6 | D, E | 24 |

## SCATS graphics

Figure 1 - SCATS graphics

## Appendix B – SCATS Traffic Data example

Site:   199  Thursday 8 September 2016        Traffic Flow filename:BEL_20160908.VS

Thursday 8 September 2016

Approach detector(s)

AM peak    1793 08:05 - 09:05    PM peak    1579 16:55 - 17:55    Daily Total   17356

## Appendix C – SIDRA Outputs example

### Figure 1: Intersection Geometry – Base model vs Option model

### Figure 2: Input Volumes Summary – Base model vs Option model

### Figure 3: Movement Summary – Base model vs Option model

### Figure 4: Phasing Summary – Base model vs Option model

## Appendix D – Key checks on SIDRA models

| Lane geometry | Lane widths | Comments |
| --- | --- | --- |
|  | Slip lane storage lengths |  |
|  | Pedestrian crossing widths (if site or approach has higher ped-crossing demands) |  |
|  | Merging/weaving lanes and lengths |  |
|  | Lane configurations (shared/dedicated movements) |  |
|  | Lane capacity |  |
| Lane movements | Approach lane to exit lane delineation |  |
|  | Approach lane to exit lane vehicle type flow consistency (e.g. bus lane on approach side should direct to bus lane on exit side) |  |
| Pedestrian | Modelled crossing width |  |
|  | Pedestrian actuation |  |
| Volumes | Traffic data source |  |
|  | Heavy vehicles % |  |
| Priorities | Vehicle to vehicle movements |  |
|  | Vehicle to pedestrian movements |  |
| Gap acceptance | Critical gap |  |
|  | Follow-up headway |  |
|  | Gap acceptance capacity model |  |
| Vehicle movement data | Approach and exit cruise speeds (and by veh type) |  |
|  | Signals coordination |  |
|  | Minimum green | In base model, existing minimum green in SCATS should be provided. In option model, 8 sec should be provided. |
|  | Early cut-off (ECO) |  |
|  | Late start |  |
| Phasing and timings | Phase sequence | In base model, current SCATS phase sequence and any overlaps are expected. |
|  | Phase times | In base model, current operating phase times are expected (and cycle time option should be ticked as ‘user-given phase times’) |
|  | Phase frequency | Based on no. of activations in existing operation, phase frequency mode (program or input) should be opted. |
|  | Yellow and red times | In base model, existing values should be provided. In option models: Yellow – 3 sec for 60km/h and 4 sec for 80km/h Red – determined based on the intersection crossing width for each turning movement. |
|  | Cycle time | In base model, ‘user-given phase times’ should be enabled. In option model, either ‘optimum cycle time’ or ‘user-given cycle time’ should be enabled. If recommended optimum cycle time (by SIDRA) seems unreasonable from practical sense, then user-given cycle time should be opted to provide sensible cycle time. |
| Outputs | Queue lengths |  |
|  | Delays |  |
|  | Degree of saturation |  |
|  | Level of service |  |