BICYCLE SECURITY

The following information is provided courtesy of Pedal Power ACT. (http://www.pedalpower.org.au/index.htm)

A Look at Locks

Each year police receive reports of thousands of bicycle thefts. How many are stolen and not reported is unknown.

At some time you will have to leave your bike unattended. There are many things you can do to reduce the chance of it being stolen. The first is to buy a lock.

It takes about one second to steal a bike without a lock. It may only be a matter of ten seconds to steal a bicycle with a poor quality lock. A good lock will delay a thief too long and they will go away and steal an easier bike instead. As a rule of thumb, if you aren't within handy reach of your bike, then lock it, preferably to an immovable object. Remember that a thief on your bike is a lot faster than you are on foot. Don't choose a quiet side street - a thief is less likely to try to circumvent your lock or remove parts if the bike is visible to passers-by.

Padlocks

The security of a padlock is generally defined by how well it resists a forceful attack. Locks are usually opened by force rather than finesse. However, some of the cheapest combination locks are easily unpicked.

Any padlock with an unhardened shackle can be cut with an ordinary hacksaw. Boltcutter resistance is determined largely by the thickness of the shackle, as well as shackle material and hardening technique. The thicker the shackle the more work and/or the bigger the boltcutters needed.

Chains

These vary from very cheap, thin and ineffective chains which could be broken by a hefty tug on the locked bike, through to heavy duty case-hardened alloy steel chains with welded links.

Cables

The most common cable is the 1.8 metre long, five millimetre thick, plastic covered self-coiling cable usually sold with a key or combination padlock. These can be cut easily with boltcutters and, with a bit of work, by sidecutters (like pliers).

Ten millimetre thick cables, usually 1.2 metres long, can be bought with integrated lock, with a separate padlock, or individually. To cut through these thicker cables takes a much more determined effort by a thief.

U-locks

U-locks are the most secure bicycle locking system commonly available. They are expensive (but not relative to the cost of replacing your bicycle) and quite heavy but are impervious to bolt cutters, hacksaws, drills, picking, prying, smashing or just about anything short of an oxy-torch. These locks are made of through-hardened steel alloys and are vinyl coated to protect the bike frame. Some U-lock manufacturers offer a cash guarantee against theft using forceful means.

All U-locks are easy to use. They are even easier to use if a carrying bracket is also fitted to your bicycle. Bear in mind that this convenience makes for greater use and hence greater protection for your bike. The lock is an extra load on your bicycle, but it takes a load off your mind, particularly if your bike travels mainly in urban areas where theft rates are higher. Their only drawback is that they are less flexible in use - you have a lesser choice of objects to which to lock your bike than with a cable.

Bicycle Identification and Police

If your bicycle is stolen then report the theft to the local police. They will want to know details such as brand, model, frame serial number, colour, accessories, component particulars etc. Record these now and keep them in a safe place at home. This information will help the police identify your bike if it should be recovered, as is often the case with stolen bikes. Pedal Power ACT has a printed form to record details of your bike. A good photograph is also an idea. Have your neighbourhood watch member assist with engraving your drivers licence number on the frame; the number prefixed by the letter A to indicate an ACT licence.

Bicycle Insurance

Most home contents insurance policies cover bicycles at home, but not elsewhere. There are some insurance companies which offer bicycle insurance, though usually it is fairly expensive, while other companies will offer an extended policy. As the policies differ between companies, it is best that you read the fine print and have your bike recorded on your policy. Insurance is payable yearly. A good lock will last forever.